C128 Memory Map

  This is as complete as possible compilation of two separate memory maps,
  and a few random sources which naturally do differ from each other.


  C128 RAM

All Banks

0000		I/O direction register
0001		I/O port, similar to C64
0002		Bank Number, Jump to SYS Address
0003-0004	SYS address, MLM register PC
0005-0009	SYS and MLM register save (SR, A, X, Y, SP)
000a		Scan-quotes flag
000b		TAB column save
000c		0 = LOAD, 1 = VERIFY
000d		Input buffer pointer / number of subscripts
000e		default DIM flag
000f		Type: FF = string, 00 = numeric
0010		Type: 80 = integer, 00 = floating point
0011		DATA scan / LIST quote / memory flag
0012		Subscript / FNxx flag
0013		0 = INPUT, $40 = GET, $98 = READ
0014		ATN sign / Comparison evaluation flag
0015		Current I/O prompt flag
0016-0017	Integer value
0018		Pointer: temporary string stack
0019-0023	Stack for temporary strings
0024-0027	Utility pointer area
0028-002c	Product area for multiplication
002d-002e	Pointer: Start-of-BASIC (bank 0)
002f-0030	Pointer: Start-of-variables (bank 1)
0031-0032	Pointer: Start-of-arrays
0033-0034	Pointer: End-of-arrays
0035-0036	Pointer string-storage (moving down)
0037-0038	Utility string pointer
0039-003a	Pointer: Limit-of-memory (bank 1)
003b-003c	Current BASIC line number
003d-003e	Textpointer: BASIC work point (chrget)
003f-0040	Utility Pointer
0041-0042	Current DATA line number
0043-0044	Current DATA address
0045-0046	Input vector
0047-0048	Current variable name
0049-004a	Current variable address
004b-004c	Variable pointer for FOR/NEXT
004d-004e	Y-save, op-save, BASIC pointer save
004f		Comparison symbol accumulator
0050-0055	Miscellaneous work area, pointers, and so on

0056-0058	Jump vector for functions
0059-0062	Miscellaneous numeric work area
0063		Accum #1 exponent
0064-0067	Accum #1 mantissa
0068		Accum #1 sign
0069		Series evaluation constant pointer
006a-006f	Accum #2 exponent, and so on
0070		Sign comparison Acc #1 versus #2
0071		Accum #1 lo-order (rounding)
0072-0073	Cassette buffer len / Seris pointer
0074-0075	Auto line number increment
0076		Graphics flag: FF = Graphics allocated
0077		Color source number
0078-0079	Temporary counters
007a-007c	DS$ descriptor
007d-007e	BASIC pseudo-stack pointer
007f		Flag: 0 = direct mode
0080-0081	DOS, USING work flags
0082		Stack pointer save for errors
0083		Graphic color source
0084		Multicolor 1 (1)
0085		Multicolor 2 (2)
0086		Graphic foreground color (13)
0087-008a	Graphic scale factors, X & Y
008b-008f	Graphic work values
0090		Status word ST
0091		Keyswitch 1A: STOP and RVS flags
		 7	STOP
		 6	Q
		 5	C=
		 4	Space
		 3	2
		 2	CTRL
		 1	<-
		 0	1

0092		Timing constant for tape ($80)
0093		Work value, monitor, LOAD / SAVE
			0 = LOAD, 1 = VERIFY
0094		Serial output, deferred character flag
0095		Serial deferred character
0096		Cassette work value
0097		Register save
0098		How many open files
0099		Input device, normally 0
009a		Output CMD device, normally 3
009b-009c	Tape parity, output-received flag
009d		I/O messages: 192 = all, 128 = commands, 64 = errors, 0 = nil
009e-009f	Tape error pointers
00a0-00a2	Jiffy clock HML
00a3-00a4	Scratch registers. (don't use)
00a5-00a6	I/O work bytes (tape)
00a7-00ab	RS-232C Receive, Misc Work Values
00a7		RS-232 Input Bit Storage, Cassette Short Count
00a8		RS-232 Bit Count In, Cassette Read Error
00a9		RS-232 Flag For Start Bit Check, Cassette Reading Zeroes
00aa		RS-232 Byte Buffer, Cassette Read Mode
00ab		RS-232 Parity Storage, Cassette Short Cnt

00ac-00ad	Pointer for tape buffer and screen scrolling
00ae-00af	Tape end address / End of program
00b0-00b1	Tape timing constants
00b2-00b3	Pointer: Start of tape buffer
00b4-00b6	RS-232 Send, Misc work values
00b4		RS-232 Bit Count
00b5		RS-232 Next Bit To Be Sent
00b6		RS-232 Byte Buffer
00b7		Number of characters in file name
00b8		Current logical file
00b9		Current secondary address
00ba		Current device
00bb-00bc	Pointer to file name
00bd		RS-232 TRNS Parity Buffer
00be		Cassette Read Block Count
00bf		Serial Word Buffer
00c0		Cassette Manual/Cntrolled Switch (Updated during IRQ)
00c1-00c2	I/O Start Address
00c3-00c4	Cassette LOAD Temps (2 bytes)
00c5		Tape Read/Write Data

00c6-00c7	BANKS: I/O data, filename
00c8-00c9	RS-232 input buffer addresses  ($0c00)
00ca-00cb	RS-232 output buffer addresses ($0d00)
00cc-00cd	Keyboard decode pointer (bank 15) ($fa80)
00ce-00cf	Print string work pointer
00d0		Number of characters in keyboard buffer
00d1		Number of programmed chars waiting
00d2		Programmed key character index
00d3		Key shift flag:
		 0	No shift
		 1	Shift
		 2	C=
		 4	Control
		 8	Alt
		15	Caps Lock

00d4		Current key code: 88 = no key
00d5		Previous key code: 88 = no key
00d6		Input from screen / from keyboard
00d7		40 / 80 columns: 0 = 40 column screen
00d8		Graphics mode code
		 000	0	Graphic 0
		 001	1		1
		 011	2		2
		 101	3		3
		 111	4		4

00d9		Character base: 0 = ROM, 4 = RAM
00da-00df	Misc work area

00e0-00e1	Pointer to screen line / cursor
00e2-00e3	Color line pointer
00e4		Current screen bottom margin
00e5		Current screen top margin
00e6		Current screen left margin
00e7		Current screen right margin
00e8-00e9	Input cursor log (row, column)
00ea		End-of-line for input pointer
00eb		Row where cursor lives
00ec		Position of cursor on screen line
00ed		Maximum screen lines (24)
00ee		Maximum screen columns (39)
00ef		Current I/O character
00f0		Previous character printed
00f1		Character color
00f2		Temporary color save
00f3		Screen reverse flag
00f4		0 = direct cursor, else programmed
00f5		Number of INSERTs outstanding
00f6		255 = Auto Insert enabled
00f7		Text mode lockout (SHFT-C=): 0 = enabled, 128 = disabled
00f8		Scrolling: 0 = enabled, 128 = disabled
00f9		Bell (CTRL-G):  0= enable, 128 = disable
00fa-00fe	Not used
00ff		Basic Scratch

0100-01ff	Processor Stack Area
0100-013e	Tape error log
0100-0124	DOS work area
0125-0138	PRINT / USING work area

0200-03ff	Vectors, buffers, Kernal RAM

0200-02a1	BASIC input buffer

			512-673	BASIC & Monitor Input Buffer (161 bytes)
	02a2-02ae	674-686	Kernal RAM: 

02a2-02ae	Bank Peek Subroutine
02af-02bd	Bank Poke Subroutine
02be-02cc	Bank Compare Subroutine
02cd-02e2	JSR to Another Bank
02e3-02fb	JMP to Another Bank
02fc-02fd	Function Execute Hook	[4c78]

0300-0301	Error Message Link	[4D3F]
0302-0303	BASIC Warm Start Link	[4DC6]
0304-0305	Crunch BASIC Tokens Link [430D]
0306-0307	Print Tokens Link	[5151]
0308-0309	Start New BASIC Code Link [4AA2]
030a-030b	Get Arithmetic Element Link [78DA]
030c-030d	Crunch FE Hook	[4321]
030e-030f	List FE Hook	[51CD]
0310-0311	Execute FE Hook [4BA9]
0312-0313	Unused
0314-0315	IRQ Vector	[FA65]
0316-0317	Break Interrupt Vector [B003]
0318-0319	NMI Interrupt Vector [FA40]
031a-031b	OPEN Vector	[EFBD]
031c-031d	CLOSE Vector	[F188]
031e-031f	Set Input Vector [F106]
0320-0321	Set Output Vector [F14C]
0322-0323	Restore I/O Vector [F226]
0324-0325	Input Vector	[EF06]
0326-0327	Output Vector	[EF79]
0328-0329	Test STOP Key	[F66E]
032a-03ab	GET Vector	[EEEB]
032c-032d	Abort I/O Vector [F222]
032e-032f	Machine Lang Monitor Link [B006]
0330-0331	LOAD Link	[F26C]
0332-0333	SAVE Link	[F54E]
0334-0335	Print Control Code Link [C7B9]
0336-0337	Print High ASCII Code Link [C805]
0338-0339	Print ESC Sequence Link [C9C1]
033a-033b	Keyscan Link	[C5E1]
033c-033d	Store Key	[C6AD]

033e-033f	Pointer to KBD Decoding Table: Unshifted [FA80 / FD29]
0340-0341	Pointer to KBD Decoding Table: Shifted   [FAD9 / FD82]
0342-0343	Pointer to KBD Decoding Table: Commodore [FB32 / FDDB]
0344-0345	Pointer to KBD Decoding Table: Control   [FB8B / FE34]  1)
0346-0347	Pointer to KBD Decoding Table: Alt       [FA80 / FD29]
0348-0349	Pointer to KBD Decoding Table: Ascii/DIN [FB4E / FD29]

    1) The value FE34 is used in German version, it doesn't change in others.

034a-0353	IRQ Keyboard Buffer (10 Bytes)  FF = No key
0354-035d	Bitmap Of TAB Stops (10 Bytes)
035e-0361	Bitmap Of Line Wraps
0362-036b	Logical File Number Table
036c-0375	Device Number Table
0376-037f	Secondary Addresse Table
0380-039e	CHRGET Subroutine
0386		CHRGOT Entry

039f-03aa	Fetch From RAM Bank 0
03ab-03b6	Fetch From RAM Bank 1
03b7-03bf	Index1 Indirect Fetch From RAM Bank 1
03c0-03c8	Index2 Indirect Fetch From RAM Bank 0
03c9-03d1	Txtptr Fetch From RAM Bank 0
03d2-03d4	Numeric Constant For BASIC
03d5		Current Bank For SYS, POKE, PEEK
03d6-03d9	INSTR Work Values
03da		Bank Pointer For String/Number CONVERT RTN
03db-03dd	Sprite: Work bytes for SSHAPE
03df		FAC#1 Overflow
03e0-03e1	Sprite: Work bytes for SPRSAV
03e2		Graphic Foreground/ Background Color Nybbles
03e3		Graphic Foreground/ Multicolor 1 Color Nybbles
03f0-03f6	DMA Link Code

ff00		MMU Configuration Register
ff01		MMU LCR: Bank 0
ff02		MMU LCR: Bank 1
ff03		MMU LCR: Bank 14
ff04		MMU LCR: Bank 14 Over RAM 1

	Page Four & Higher Declarations (Beginning Of Bankable RAM)


Bank 0

0400-07e7	VIC 40-Column Text Screen
07e8-07ff	Sprite Identity Pointers For Text Mode
0800-09ff	BASIC Pseudo Stack (gosub and loop addresses and commands)

0a0c		CIA 1 Interrupt Log
0a0d		CIA 1 Timer Ensbled
0a0f-0a17	RS-232 Work Values
0a18		RS-232 Receive Pointer
0a19		RS-232 Input Pointer
0a1a		RS-232 Transmit Pointer
0a1b		RS-232 Send Pointer
0a1d-0a1f	Sleep Countdown, FFFF = disable
0a20		Keyboard Buffer Size
0a21		Screen Freeze Flag
0a22		Key Repeat: 128 = all, 64 = none
0a23		Key Repeat Timing
0a24		Key Repeat Pause
0a25		Graphics / Text Toggle Latch
0a26		40-Col Cursor Mode
0a27-0a2a	40-Col Blink Values
0a2b		80-Col Cursor Mode
0a2c		40-Col Video $D018 Image
0a2d
0a2e-0a2f	80-Col Pages-Screen, Color
0a40-0a5a	40/80 Pointer Swap (to E0-FA)

0a60-0a6d	40/80 Data Swap (0354-0361)

0ac0		PAT Counter
0ac1-0ac4	ROM Physical Address Table

0b00-0bbf	Cassette Buffer
0bc0-0bff
0c00-0dff	RS-232 Input, Output Buffers
0e00-0fff	System Sprites (56-63)
1000-1009	Programmed Key Lenghts
100a-10ff	Programmed Key Definitions
1100-1130	DOS Command Staging Area
1131-116e	Graphics Work Area

116f		Trace Mode: FF = on
1170-1173	Renumbering Pointers
1174-1177	Directory Work Pointers
1178-1197	Graphics Index
117a-117b	Float-fixed Vector [849F]
117c-117d	Fixed-float Vector [793C]
117e-11d5	Sprite Motion Tables (8 x 11 bytes)
11d6-11e5	Sprite X/Y Positions
11e6		Sprite X-High Positions
11e7-11e8	Sprite Bumb Masks (sprite - backgnd)
11e9-11ea	Light Pen Values, X and Y
11eb		CHRGEN ROM Page, Text Mode [D8]
11ec		CHRGEN ROM Page, Graphics Mode [D0]
11ed		Secondary Address For RECORD
11ee-11ff	Unused

1204-1207	PU Characters (,.$)
120b-120c	TRAP Address, FFFF = none
1210-1211	End of Basic, Bank 0
1212-1213	Basic Program Limit [FF00]
1214-1217	DO Work Pointers
1218-121a	USR Program Jump [7D28]
121b-121f	RND Seed Value

1222		Sound Tempo
122f		Music Sequencer (Envelope)

1234-1237	Note Image
1239-123e	Current Envelope Pattern
123f-1270	Envelope Tables
123f-1248	AD(SR) Pattern
1249-1252	(AD)SR Pattern
1253-125c	Waveform Pattern
125d-1266	Pulse Width Lo Pattern
1267-1270	Pulse Width Hi Pattern
1271-1274	Note: xx, xx, volume
1275		Previous Volume Image
1276-1278	Collision IRQ Task Table
1279-127e	Collision IRQ Address Tables
127f		Collision Mask
1280		Collision Work Value

12b1		PEN Work Value
12ff		?
1300-17ff	Unused
1800-1bff	Reserved for Key Functions
1c00-fbff	BASIC RAM Memory (Text)
1c00-1ff7	Video Color Matrix For Graphics Mode
1ff8-1fff	Sprite Identity Pointers For Graphics Mode
2000-3fff	Screen Memory For Graphics Mode
4000-fbff	BASIC RAM Memory (with graphics enabled)


Bank 1

0400-fbff	BASIC Variables, Arrays, And Strings


Bank 14
The same as Bank 15, except:

d000-dfff	Character Generator ROM


Bank 15

4000-cfff	BASIC ROM
d000-d030	VIC, 40 Col Video Chip 8564 (NTSC) or 8566 (PAL)
d400-d41c	SID Sound Chip 6581
d500-d50b	MMU, Memory Management Unit 8722
d600-d601	VDC, 80 Col Video Controller 8563
d800-d8e7	Color Nybbles For VIC Text Screen
dc00-dc0f	CIA 1 (IRQ), 6526
dd00-dd0f	CIA 2 (NMI), 6526
df00-df0a	DMA Slot
e000-ffff	KERNAL ROM
ff00-ff04	MMU
ff05-ffff	Transfer, Jump Table


	*****

502 COMMODORE 128

This chapter provides the memory maps for both C128 and C64 modes. A memory
map tells you exactly how memory is laid out internally in both RAM and ROM.
It tells you exactly what resides in each memory location. The memory map
directs you in finding address vectors for routines and entry points and provi-
des information about the general layout of the computer. The memory map is
probably the most vital programming tool.

Refer to the memory map whenever you need directions throughout the memory of 
your Commodore 128. Addresses listed with more than one address label are used
for more than one purpose. To BASIC, the variable has one purpose; to the Mac-
hine Language Monitor, it may have another.

The conventions used for the memory maps are as follows:

Column 1	Column 2	Column3		Column 4
MEMORY
ADDRESS		HEXADECIMAL	DECIMAL
LABEL		ADDRESS		ADDRESS		DESCRIPTION

	See Appendix K for the Z80 memory map for CP/M on the Commodore 128.


		C128 MEMORY MAP

MEMORY ADDRESS	  ADDRESS
LABEL		HEX	DEC	DESCRIPTION

D6510		0000	0	6510 Data Direction Register
R6S10		0001	1	6510 Data Register
BANK		0002	2	Token 'SEARCH' looks for, or Bank #
PC_HI		0003	3	Address for BASIC SYS command or MONITOR and
				LONG CALL/JUMP Routines
PC_LO		0004	4	Address
S_REG		0005	5	STATUS REG Temp
A_REG		0006	6	.A REG Temp
X_REG		0007	7	.X REG Temp
Y_REG		0008	8	.Y REG Temp
STKPTR		0009	9	Stack Pointer Temp


		BASIC ZERO PAGE STORAGE

INTEGR		0009	9
CHARAC				Search Character
ENDCHR		000A	10	Flag: Scan For Quote at End Of String
TRMPOS		000B	11	Screen Column from Last Tab
VERCIC		000C	12	Flag: 0 = LOAD, 1 = VERIFY

COUNT		000D	13	Input Buf.ptr / # of Subscripts

DIMFLG		000E	14	Flag: Default Array Dimension
VALTYP		000F	15	DATA Type: $FF=String, $00 = Numeric
INTFLG		0010	16	DATA Type: $00=Float.Pt, $80 = Integer
GARBFL		0011	17	Flag: DATA Scan/ LIST Quote/ Garbage Collection

DORES
SUBFLG		0012	18	Flag: Subscript Ref. / User Func. Call

INPFLG		0013	19	Flag: $00=INPUT, $40=GET, $98 = READ

DOMASK		0014	20
TANSGN				Flag: TAN Sign / Comparison Result

CHANNL		0015	21
POKER		0016	22
LINNUM				Temp Integer Value
TEMPPT		0018	24	Pointer: Temp String Stack
LASTPT		0019	25	Last Temp String Address
TEMPST		001B	27	Stack For Temp Strings
INDEX		0024	36	Utility Pointer Area
INDEX1
INDEX2		0026	38
RESHO		0028	40	Floating Pt. Product of Multiply
RESMOH		0029	41
ADDEND		002A	42
RESMO
RESLO		002B	43
TXTTAB		002D	45	Pointer: Start Of BASIC Text
VARTAB		002F	47	Pointer: Start Of BASIC Variables

ARYTAB		0031	49	Pointer: Start Of BASIC Arrays
STREND		0033	51	Pointer: End Of BASIC Arrays + 1

FRETOP		0035	53	Pointer: Bottom of String Storage
FRESPC		0037	55	Utility String Pointer
MAX_MEM_1	0039	57	Top of String/Variable Bank (Bank 1)

CURLIN		003B	59	Current BASIC Line Number
TXTPTR		003D	61	Pointer to BASIC Text used by CHRGET,etc.
FORM		003F	63	Used by PRINT USING
FNDPNT				Pointer to Item Found By Search

DATLIN		0041	65	Current DATA Line Number
DATPTR		0043	67	Current DATA Item Address
INPPTR		0045	69	Vector: INPUT Routine
VARNAM		0047	71	Current BASIC Variable Name
FDECPT		0049	73
VARPNT				Pointer: Current BASIC Variable DATA

LSTPNT		004B	75
FORPNT				Pointer: Index Variable For FOR/NEXT

ANDMSK
EORMSK		004C	76
VARTXT		004D	77
OPPTR
OPMASK		004F	79
GRBPNT		0050	80
TEMPF3
DEFPNT
DSCPNT		0052	82
		0054	84

HELPER		0055	85	Flags 'HELP' or 'LIST'
JMPER		0056	86
		0057	87
OLDOV		0058	88
TEMPF1		0059	89
PTARG1				Multiply defined for INSTR
PTARG2		005B	91
STRl		005D	93
STR2		0060	96
POSITN		0063	99
MATCH		0064	100

ARYPNT		005A	90
HIGHDS
HIGHTR		005C	92
TEMPF2		005E	94
DECCNT		005F	95	Number of Digits after the Decimal Point
TENEXP		0060	96
T0				ML MONITOR Z.P. Storage in FAC

GRBTOP		0061	97
DPTFLG				Decimal Point Flag
LOWTR
EXPSGN		0062	98
FAC		0063	99

DSCTMP
LEFT_FLAG			Paint-Left Flag
FACEXP				FAC#1 Exponent
Tl				MONITOR Z.P. Storage in FAC
RIGHT_FLAG	0064	100	Paint-Right Flag
FACHO				FAC#1 Mantissa
FACMOH		0065	101
INDICE		0066	102
FACMO
T2				MONITOR Z.P. Storage in FAC
FACLO		0067	103
FACSGN		0068	104	FAC#1 Sign
DEGREE		0069	105
SGNFLG				Pointer: Series-Eval. Constant
ARGEXP		006A	106	FAC#2 Exponent
ARGHO		006B	107	FAC#2 Mantissa
ARGMOH		006C	108
INIT_AS_0			Just a count for INIT

ARGMO		006D	109
ARGLO		006E	110
ARGSGN		006F	111	FAC#2 Sign
STRNGI		0070	112
ARISGN				Sign Comparison Result: FAC#1 vs #2

FACOV		0071	113	FAC#1 Low-Order (Rounding)
STRNG2		0072	114
POLYPT
CURTOL
FBUFPT				Pointer: Cassette Buffer
AUTINC		0074	116	Inc. Val for AUTO (0 = Off)
MVDFLG		0076	118	Flag If 10K HIRES Allocated
Z_P_TEMP_1	0077	119	PRINT USING's Leading Zero Counter
				MOVSPR & Sprite Temporary
				MID$ Temporary

HULP		0078	120	Counter
KEYSIZ
SYNTMP		0079	121	Used as Temp For Indirect
DSDESC		007A	122	Descriptor for DS$
TXTPTR				MONITOR Z.P. Storage
TOS		007D	125	Top of Run Time Stack
RUNMOD		007F	127	Flags Run/Direct Mode
PARSTS		0080	128	DOS Parser Status Word
POINT				USING's Pointer to Dec.Pt

PARSTX		0081	129
OLDSTK		0082	130


		BASIC Z-P STORAGE FOR GRAPHIC COMMANDS

COLSEL		0083	131	Current COLOR Selected

MULTICOLOR	0084	132
MULTICOLOR_2	0085	133
FOREGROUND	0086	134
SCALE_X		0087	135	Scale Factor In X
SCALE_Y		0089	137	Scale Factor In Y
STOPNB		008B	139	Stoppaint if not Background/Not same color
GRAPNT		008C	140
VTEMPI		008E	142
VTEMP2		008F	143


		KERNAL/EDITOR STORAGE

STATUS		0090	144	I/O Operation Status Byte
STKEY		0091	145	STOP KEY Flag
SVXT		0092	146	Tape Temporary
VERCK		0093	147	LOAD or VERIFY Flag
C3P0		0094	148	Serial Buffered Char Flag
BSOUR		0095	149	Char Buffer For Serial
SYNO		0096	150	Cassette Sync #
XSAV		0097	151	Temp For BASIN
LDTND		0098	152	Index to Logical File
DFLTN		0099	153	Default Input Device #
DFLTO		009A	154	Default Output Device #
PRTY		009B	155	Cassette Parity
DPSW		009C	156	Cassette Dipole Switch
MSGFLG		009D	157	OS Message Flag
PTR1		009E	158	Cassette Error Pass1
T1				Temporary 1
PTR2		009F	159	Cassette Error Pass2
T2				Temporary 2
TIME		00A0	160	24 Hour Clock In 1/60th Seconds
R2D2		00A3	163	Serial Bus Usage

PCNTR				Cassette
BSOUR1		00A4	164	Temp used by Serial Routine
FIRT
COUNT		00A5	165	Temp used by Serial Routine
CNTDN				Cassette Sync Countdown
BUFPT		00A6	166	Cassette Buffer Pointer

INBIT		00A7	167	RS-232 RCVR Input Bit Storage
SHCNL				Cassette Short Count
BITCI		00A8	168	RS-232 RCVR Bit Count In
RER				Cassette Read Error
RINONE		00A9	169	RS-232 RCVR Flag For Start Bit Check
REZ				Cassette Reading Zeroes
RIDATA		00AA	170	RS-232 RCVR Byte Buffer
RDFLG				Cassette Read Mode
RIPRTY		00AB	171	RS-232 RCVR Parity Storage
SHCNH				Cassette Short Cnt
SAL		00AC	172	Pointer: Tape Buffer / Screen Scrolling
SAH		00AD	173
EAL		00AE	174	Tape End Addresses / End of Program
EAH		00AF	175
CMP0		00B0	176	Tape Timing Constants
TEMP		00B1	177
TAPE1		00B2	178	Address of Tape Buffer
BITTS		00B4	180	RS-232 TRNS Bit Count
SNSW1
NXTBIT		00B5	181	RS-232 TRNS Next Bit To Be Sent
DIFF
RODATA		00B6	182	RS-232 TRNS Byte Buffer
PRP
FNLEN		00B7	183	LENGTH Current File N Str
LA		00B8	184	Current File Logical Addr
SA		00B9	185	Current File 2nd Addr
FA		00BA	186	Current File Primary Addr
FNADR		00BB	187	Addr Current File Name Str
ROPRTY		00BD	189	RS-232 TRNS Parity Buffer
OCHAR
FSBLK		00BE	190	Cassette Read Block Count
DRIVE		00BF	191
MYCH				Serial Word Buffer
CAS1		00C0	192	Cassette Manual/Cntrled Switch (Updated during IRQ)
TRACK		00C1	193
STAL				I/O Start Address (LO)
SECTOR		00C2	194
STAH				I/O Start Address (HI)
MEMUSS		00C3	195	Cassette LOAD Temps (2 bytes)
DATA		00C5	197	Tape Read/Write Data

BA		00C6	198	Bank For Current LOAD/SAVE/VERIFY Operation
FNBANK		00C7	199	Bank Where Current FN is found (at 'FNADR')
RIBUF		00C8	200	RS-232 Input Buffer Pointer
ROBUF		00CA	202	RS-232 Output Buffer Pointer


		GLOBAL SCREEN EDITOR VARIABLES

KEYTAB		00CC	204	Keyscan Table Pointer
IMPARM		00CE	206	PRIMM Utility String Pointer
NDX		00D0	208	Index to Keyboard Queue
KYNDX		00D1	209	Pending Function Key Flag
KEYIDX		00D2	210	Index Into Pending Function Key String
SHFLAG		00D3	211	Keyscan Shift Key Status
SFDX		00D4	212	Keyscan Current Key Index
LSTX		00D5	213	Keyscan Last Key Index
CRSW		00D6	214	<CR> Input Flag	
MODE		00D7	215	40/80 Column Mode Flag
GRAPHM		00D8	216	Text/Graphic Mode Flag
CHAREN		00D9	217	RAM/ROM VIC Character Fetch Flag (Bit-2)


	THE FOLLOWING LOCATIONS ARE SHARED BY SEVERAL EDITOR ROUTINES.

SEDSAL		00DA	218	Pointers For MOVLIN
BITMSK		00DA	218	Temporary For TAB & LINE WRAP Routines
SAVER		00DB	219	Another Temporary Place To Save A Reg.
SEDEAL		00DC	220
SEDT1		00DE	222	SAVPOS
SEDT2		00DF	223
KEYSIZ		00DA	218	Programmable Key Variables
KEYLEN		00DB	219
KEYNUM		00DC	220
KEYNXT		00DD	221
KEYBNK		00DE	222
KEYTMP		00DF	223


		LOCAL SCREEN EDITOR VARIABLES.
	These are swapped out to $0a40 when screen (40/80) mode changes.

PNT		00E0	224	Pointer to Current Line (Text)
USER		00E2	226	Pointer to Current Line (Attribute)

SCBOT		00E4	228	Window Lower Limit
SCTOP		00E5	229	Window Upper Limit
SCLF		00E6	230	Window Left Margin
SCRT		00E7	231	Window Right Margin
LSXP		00E8	232	Current Input Column Start
LSTP		00E9	233	Current Input Line Start
INDX		00EA	234	Current Input Line End
TBLX		00EB	235	Current Cursor Line
PNTR		00EC	236	Current Cursor Column
LINES		00ED	237	Maximum Number of Screen Lines
COLUMNS		00EE	238	Maximum Number of Screen Columns
DATAX		00EF	239	Current Character to Print
LSTCHR		00F0	240	Previous Char Printed (For <ESC> Test)
COLOR		00F1	241	Curr Attribute to Print (Default FGND Color)
TCOLOR		00F2	242	Saved Attrib to Print ('INSERT' & 'DELETE')

RVS		00F3	243	Reverse Mode Flag
QTSW		00F4	244	Quote Mode Flag
INSRT		00F5	245	Insert Mode Flag
INSFLG		00F6	246	Auto-Insert Mode Flag
LOCKS		00F7	247	Disables <Shift><C*>, <CTRL> S
SCROLL		00F8	248	Disables Screen Scroll, Line Linker
BEEPER		00F9	249	Disables <CTRL> G

FREKZP		00FA	250	Free Zero Page reserved for applications
				software ($FA-$FE)
LOFBUF		00FF	255


		BASIC/DOS INTERFACE VARS

BAD		0100	256	Tape Read Errors
FBUFFR				Area to build filename in (16 bytes)
XCNT		0110	272	DOS Loop Counter

DOSF1L		0111	273	DOS Filename 1 Len
DOSDS1		0112	274	DOS Disk Drive 1
DOSF2L		0113	275	DOS Filename 2 Len
DOSDS2		0114	276	DOS Disk Drive 2
DOSF2A		0115	277	DOS Filename 2 Addr
DOSOFL		0117	279	BLOAD/BSAVE Starting Address
DOSOFH		0119	281	....	and Ending Address
DOSLA		011B	283	DOS Logical Addr
DOSFA		011C	284	DOS Phys Addr
DOSSA		011D	285	DOS Sec. Addr
DOSRCL		011E	286	DOS Record Length
DOSBNK		011F	287
DOSDID		0120	288	DOS Disk ID
DIDCHK		0122	290	DOS DSK ID FLG SPACE Used by PRINT USING
BNR		0123	291	Pointer to Begin. NO.
ENR		0124	292	Pointer to End NO.
DOLR		0125	293	Dollar Flag
FLAG		0126	294	Comma Flag
SWE		0127	295	Counter
USGN		0128	296	Sign Exponent
UEXP		0129	297	Pointer to Exponent
VN		012A	298	# Of Digits Before Decimal Point
CHSN		012B	299	Justify Flag
VF		012C	300	# Of Pos Before Decimal Point (Field)
NF		012D	301	# Of Pos After Decimal Point (Field)
POSP		012E	302	+/- Flag (Field)
FESP		012F	303	Exponent Flag (Field)
ETOF		0130	304	Switch
CFORM		0131	305	Char Counter (Field)
SNO		0132	306	Sign No
BLFD		0133	307	Blank/Star Flag
BEGFD		0134	308	Pointer to Begin of Field
LFOR		0135	309	Length of Format
ENDFD		0136	310	Pointer to End Of Field
SYSTK		0137	311	System Stack ($0137-$01FF)
BUF		0200	512	Input Buffer: BASIC & MONITOR
FETCH		02A2	674	LDA(-),Y From Any Bank
FETCHVEC	02AA	682
STASH		02AF	687	STA(-),Y to Any Bank
STAVEC		02B9	697
CMPARE		02C8	702	CMP(-),Y to Any Bank
CMPVEC		02C8	712
JSRFAR		02CD	716	JSR XXXX to Any Bank & Return
JMPFAR		02E3	739	JMP XXXX to Any Bank


		VECTORS

ESC_FN_VEC	02FC	764	Vector For Additional Function Routines
K EC		02FE	766	Vector For Function Cart.
IERROR		0300		Users
		0302		(ERR IN .X)
ICRNCH		0304	772	Vector to Crunch
			774	Vector to List BASIC Text
			776	Vector to Gone (BASIC Char
			778	Vector to BASIC Token
			780	Vector to Escape-Token
		030E	782	LIST
IESCEX		0310	784	... And Execute.
IIRO		0314	788	IRQ RAM Vector
IBRK		0316	790	BRK INSTR RAM Vector
INMI		0318	792	NMI Vector
IOPEN		031A	794	KERNAL OPEN Routine Vector

			796	KERNAL CLOSE Routine Vector

			798	KERNAL CHKIN Routine Vector
			800	KERNAL CHKOUT Routine

CLRCH		0322	Vector
VECTOR

IBASIN		0324	804	KERNAL CHRIN Routine Vector
IBSOUT		0326	806	KERNAL CHROUT Routine Vector
ISTOP		0328	808	KERNAL STOP Routine Vector
IGETIN		032A	810	KERNAL GETIN Routine Vector
ICLALL		032C	812	KERNAL CLALL Routine Vector
EXMON		032E	814	Monitor Command Vector
ILOAD		0330	816	KERNAL LOAD Routine Vector
ISAVE		0332	818	KERNAL SAVE Routine Vector


	EDITOR INDIRECT VECTORS

CTLVEC		0334	820	Editor: PRINT 'CONTRL' Indirect
SHFVEC		0336	822	Editor: PRINT 'SHIFTD' Indirect
ESCVEC		0338	824	Editor: PRINT 'ESCAPE' Indirect
KEYVEC		033A	826	Editor: Keyscan Logic Indirect
KEYCHK		033C	828	Editor: Store Key Indirect
DECODE		033E	830	Vectors to Keyboard Matrix Decode Tables
KEYD		034A	842	IRQ Keyboard Buffer (10 Bytes)

TABMAP		0354	852	Bitmap Of TAB Stops (10 Bytes, $0354-D)
BITABL		035E	862	Bitmap Of Line Wraps

				TABMAP and BITABL get swapped to $0A60 when
				screen 40/80 mode is changed.

LAT		0362	866	Logical File Numbers
FAT		036C	876	Primary Device Numbers
SAT		0376	886	Secondary Addresses
CHRGET		0380	896
CHRGOT		0386	902
QNUM		0390	912


	INDIRECT LOAD SUBROUTINE AREA

INDSUB_RAM0	039F	927	Shared ROM Fetch Sub
INDSUB_RAM1	03AB	939	Shared ROM Fetch Sub
INDIN1_RAM1	03B7	950	Index1 Indirect Fetch
INDIN2		03C0	959	Index2 Indirect Fetch
INDIXT		03C9	968	Txtptr

ZERO		03D2	977	Numeric Constant For BASIC
CURRENT_BANK	03D5	979	Context For SYS,POKE,PEEK From Bank Cmmd
TMPDES		03D6	980	Temp For INSTR
FIN_BANK	03DA	984	Bank Pointer For String/Number CONVERT RTN
SAVSIZ		03DB	985	Temp Work Locations for SSHAPE
BITS		03DF	989	FAC#1 OVERFLOW DIGIT
SPRTMP_1	03E0	990	Temp For SPRSAV
SPRTMP_2	03E1	991
FG_BG		03E2	992	Packed Foreground/ Background Color Nybbles
FG_MC1		03E3	993	Packed Foreground/ Multicolor 1 Color Nybbles


	Page Four & Higher Declarations (Beginning Of Bankable RAM)

VICSCN		0400	1024	VIDEO MATRIX #1: VIC 40-Column Text Screen
				$0400-$07FF

		0800	2048	BASIC RUN-TIME STACK (512 BYTES)
				$0800-$09FF


	ABSOLUTE KERNAL VARIABLES

SYSTEM_VECTOR	0A00	2560	Vector to Restart System (BASIC Warm)
DEJAVU		0A02	2562	KERNAL Warm/Cold Init'n Status Byte
PALNTS		0A03	2563	PAL/NTSC System Flag
INIT_STATUS	0A04	2564	Flags RESET vs. NMI Status for init'n rtns
MEMSTR		0A05	2565	Ptr to Bottom of Avail. Memory in System Bank
MEMSIZ		0A07	2567	Ptr to Top of Available Memory in System Bank
IRQTMP		0A09	2569	Tape Handler preserves IRQ Indirect here
CASTON		0AOB	2571	TOD Sense during tape operations
KIKA26		0AOC	2572	Tape Read Temporary
STUPID		0AOD	2573	Tape Read D1IRQ Indicator
TIMOUT		0AOE	2574	Fast Serial Timeout Flag
ENABL		0A0F	2575	RS-232 Enables

M51CTR		0A10	2576	RS-232 Control Register
MSICDR		0A11	2577	RS-232 Command Register
MSIAJB		0A12	2578	RS-232 User Baud Rate
RSSTAT		0A14	2580	RS-232 Status Register
BITNUM		0A15	2581	RS-232 Number of Bits To Send
BAUDOF		0A16	2582	RS-232 Baud Rate Full Bit Time (Created by OPEN)
RIDBE		0A18	2584	RS-232 Input Buffer Index to End
RIDBS		0A19	2585	RS-232 Input Buffer Index to Start
RODBS		0A1A	2586	RS-232 Output Buffer Index to Start
RODBE		0A1B	2587	RS-232 Output Buffer Index to End
SERIAL		0A1C	2588	Fast Serial Internal/External Flag
TIMER		0A1D	2589	Decrementing Jiffie Register


	GLOBAL ABSOLUTE SCREEN EDITOR DECLARATIONS

XMAX		0A20	2592	Keyboard Queue Maximum Size
PAUSE		0A21	2593	CTRL-S Flag
RPTFLG		0A22	2594	Enable Key Repeats
KOUNT		0A23	2595	Delay Between Key Repeats
DELAY		0A24	2596	Delay Before a Key Starts Repeating
LSTSHF		0A25	2597	Delay Between <C=><SHFT> Toggles
BLNON		0A26	2598	VIC Cursor Mode (Blinking, Solid)
BLNSW		0A27	2599	VIC Cursor Disable
BLNCT		0A28	2600	VIC Cursor Blink Counter
GDBLN		0A29	2601	VIC Cursor Character Before Blink
GDCOL		0A2A	2602	VIC Cursor Color Before Blink
CURMOD		0A2B	2603	VDC Cursor Mode (when enabled)
VMl		0A2C	2604	VIC Text Screen/Character Base Pointer
VM2		0A2D	2605	VIC Bit-Map Base Pointer
VM3		0A2E	2606	VDC Text Screen Base
VM4		0A2F	2607	VDC Attribute Base
LINTMP		0A30	2608	Temporary Pointer to Last Line For LOOP4
SAV80A		0A31	2609	Temporary For 80-Col Routines
SAV80B		0A32	2610	Temporary For 80-Col Routines
CURCOL		0A33	2611	VDC Cursor Color Before Blink
SPLIT		0A34	2612	VIC Split Screen Raster Value
FNADRX		0A35	2613	Save .X During Bank Operations
PALCNT		0A36	2614	Counter for PAL Systems (Jiffie adjustment)
SPEED		0A37	2615	Save System Speed During Tape and Serial Ops
SPRITES		0A38	2616	Save Sprite Enables During Tape and Serial Ops
BLANKING	0A39	2617	Save Blanking Status During Tape Ops
HOLD_OFF	0A3A	2618	Flag set by user to resrv full control of VIC
LDTBI_SA	0A3B	2619	Hi byte:SA Of VIC Scrn (Use W/VMI to move scrn)
CLR_EA_LO	0A3C	2620	8563 Block Fill
CLR_EA_HI	0A3D	2621	8563 Block Fill
		0A40	2624	$0A40-$0A7F Reserved Swap Area For Screen
				Variables When (40/80) Mode Changes
				MONITOR's domain

XCNT		0A80	2688	Compare Buffer (32 bytes)
HULP		0AA0	2720
FORMAT		0AAA	2730
LENGTH		0AAB	2731	ASM/DIS
MSAL		0AAC	2732	For Assembler
SXREG		0AAF	2735	1 Byte Temp used all over
SYREG		0AB0	2736	1 Byte Temp used all over
WRAP		0AB1	2737	1 Byte Temp for Assembler
XSAVE		0AB2	2738	Save .X here during Indirect Subroutine Calls
DIRECTION	0AB3	2739	Direction Indicator For 'TRANSFER'
COUNT		0AB4	2740	Parse Number Conversion
NUMBER		0AB5	2741	Parse Number Conversion
TEMPS		0AB7	2743	Parse Number Conversion


	FUNCTION KEY ROM CARD TABLES

CURBNK		0AC0	2752	Current Function Key ROM Bank Being Polled

PAT		0AC1	2753	Physical Address Table (IDS OF LOGGED-IN CARDS)

DK_FLAG		0AC5	2757	Reserved For Foreign Screen Editors
		0AC6	2758	$0AC6-$0AFF Reserved For System

TBUFFR		0B00	2810	Cassette Buffer (192 BYTES)
				$0B00-$0BC0, This page also used as a buffer
				for the disk auto-boot.

RS232I		0C00	3072	RS-232 Input Buffer

RS2320		0D00	3328	RS-232 Output Buffer
		0E00	3584	Sprite Definition Area (Must be below $1000)
				$0E00-$0FFF, 512 Bytes

PKYBUF		1000	4096	Programmable Function Key Lengths Table For
				10 Keys (F1-F8, <SHIFT RUN>, HELP)

PKYDEF		100A	4106	Programmable Function Key Strings


	DOS/VSP AREA


DOSSTR		1100	4352	DOS OUTPUT STR. BUF
				48 Bytes to Build DOS String

VWORK		1131	4401	Graphics Vars

XYPOS		1131	4401
XPOS		1131	4401	Current X Position
YPOS		1133	4403	Current Y Position
XDEST		1135	4405	X-Coordinate Destination
YDEST		1137	4407	Y-Coordinate Destination
XYABS		1139	4409	Line Drawing Variables
XABS		1139	4409
YABS		113B	4411
XYSGN		113D	4413
XSGN		113D	4413
YSGN		113F	4415
FCT		1141	4417
ERRVAL		1145	4421
LESSER		1147	4423
GREATR		1148	4424


	ANGLE ROUTINE VARIABLES

ANGSGN		1149	4425	Sign Of Angle
SINVAL		114A	4426	Sine Of Value Of Angle


	DOS/VSP AREA

COSVAL		114C	4428	Cosine of Value of Angle
ANGCNT		114E	4430	Temps For Angle Distance Routines


		BASIC GRAPHIC VARIABLES.
	The following 24 bytes are multiply defined.

	CIRCLE DRAWING VARIABLES

XCIRCL		1150	4432	CIRCLE Center, X Coordinate
YCIRCL		1152	4434	CIRCLE Center, Y Coordinate
XRADUS		1154	4436	X Radius
YRADUS		1156	4438	Y Radius
ROTANG		1158	4440	Rotation Angle
ANGBEG		115C	4444	Arc Angle Start
ANGEND		115E	4446	Arc Angle End
XRCOS		1160	4448	X Radius * COS(Rotation Angle)
YRSIN		1162	4450	Y Radius * SIN(Rotation Angle)
XRSIN		1164	4452	X Radius * SIN(Rotation Angle)
YRCOS		1166	4454	Y Radius * COS(Rotation Angle)

	BASIC GENERAL USE PARAMETERS

XCENTR		1150	4432
YCENTR		1152	4434
XDIST1		1154	4436
YDIST1		1156	4438
XDIST2		1158	4440
YDIST2		115A	4442
DISEEND		115C	4444	Placeholder
COLCNT		115E	4446	Char's Col. Counter
ROWCNT		115F	4447
STRCNT		1160	4448

	BOX-DRAWING VARIABLES

XCORDI		1150	4432	POINT I X-Coord.
YCORDl		1152	4434	POINT I Y-Coord.
BOXANG		1154	4436	Rotation Angle
XCOUNT		1156	4438
YCOUNT		1158	4440
BXLENG		115A	4442	Length of a side
XCORD2		115C	4444
YCORD2		115E	4446

	SHAPE AND MOVE-SHAPE VARIABLES

KEYLEN		1151	4433
KEYNXT		1152	4434
STRSZ		1153	4435	String Len

GETTYP		1154	4436	Replace Shape Mode
STRPTR		1155	4437	String Pos'n Counter
OLDBYT		1156	4438	Old Bit Map byte
NEWBYT		1157	4439	New String or Bit Map Byte
		1158	4440	Placeholder

XSIZE		1159	4441	SHAPE Column Length
YSIZE		115B	4443	SHAPE Row Length
XSAVE		115D	4445	Temp For Column Length
STRADR		115F	4447	Save SHAPE String Descriptor
BITIDX		1161	4449	Bit Index Into Byte


	BASIC GRAPHIC VARIABLES

CHRPAG		1168	4456	HIGH BYTE: ADDR OF CHARROM For 'CHAR' CMD.

BITCNT		1169	4457	Temp For GSHAPE
SCALEM		116A	4458	SCALE Mode Flag
WIDTH		116B	4459	Double Width Flag
FILFLG		116C	4460	Box Fill Flag
BITMSK		116D	4461	Temp For Bit Mask
NUMCNT		116E	4462
TRCFLG		116F	4463	Flags Trace Mode
RENUM_TMP_1	1170	4464	A Temp For Renumber
RENUM_TMP_2	1172	4466	A Temp For Renumber
T3		1174	4468
T4		1175	4469

VTEMP3		1177	4471	Graphic Temp Storage
VTEMP4		1178	4472
VTEMP5		1179	4473
ADRAY1		117A	4474	Ptr to routine: Convert Float -> Integer
ADRAY2		117C	4476	Ptr to routine: Convert Integer -> FLOAT
SPRITE_DATA	117E	4478	Sprite Speed/Direction Tables ($117E-D5)

VIC_SAVE	11D6	4566	Copy of VIC Reg's, Used to update chip during
				retrace (21 bytes, $11D6-EA)

UPPER_LOWER	11EB	4587	Pointer to Upper/Lower Char Set for CHAR
UPPER_GRAPHIC	11EC	4588	Ptr. to Upper/Graphic Char Set
DOSSA		11ED	4589	Temp storage for file SA during RECORD cmd


	BASIC GENERAL NON-ZP STORAGE

OLDTXT		1220	4608	Previous BASIC Line
			4610	Pointer: BASIC Statement for CONTINUE


	PRINT USING DECLARATIONS

PUCHRS		1204	4612
PUFILL		1204	4612	PRINT USING Fill Symbol
PUCOMA		1205	4613	PRINT USING Comma Symbol
PUDOT		1206	4614	PRINT USING D.P. Symbol
PUMONY		1207	4614	Print Using Monetary Symbol
ERRNUM		1208	4616	Used by Error Trapping Routine - Last Err No
ERRLIN		1209	4617	Line # of Last Error. $FFFF if No Error

TRAPNO		120B	4619	Line to go to on error - $FFFF if none set

TMPTRP		120D	4621	Hold Trap # of Tempor.
ERRTXT		120E	4622
TEXT_TOP	1210	4624	Top of Text Pointer
MAX_MEM_0	1212	4626	Highest Address Available to BASIC in RAM 0

TMPTXT		1214	4628	Used by DO-LOOP. Could be Mult. Assigned
TMPLIN		1216	4630
USRPOK		1218	4632
RNDX		121B	4635
CIRCLE_SEGMENT	1220	4640	Degrees Per CIRCLE 51:6MENT
DEJAVU		1221	4641	'Cold' or 'Warm' Reset Status


	BASIC STORAGE FOR MUSIC VECTORS

TEMPO_RATE	1222	4642
VOICES		1223	4643
NTIME		1229	4649
OCTAVE		122B	4651
SHARP		122C	4652
PITCH		122D	4653
VOICE		122F	4655
WAVE0		1230	4656
DNOTE		1233	4659
FLTSAV		1234	4660
FLTFLG		1238	4664
NIBBLE		1239	4665
TONNUM		123A	4666

TONVAL		123B	4667
PARCNT		123E	4668
ATKTAB		123F	4669
SUSTAB		1249	4681
WAVTAB		1253	4691
PULSLW		125D	4701
PULSHI		1267	4711
FILTERS		1271	4721


	INTERRUPT VECTORS

INT_TRIP_FLAG	1276	4726
INT_ADR_LO	1279	4729
INT_ADR_HI	127C	4732
INTVAL		127F	4735
COLTYP		1280	4736


	BASIC SOUND COMMAND VARS

SOUND_VOICE	1281	4737
SOUND_TIME_LO	1282	4738
SOUND_TIME_HI	1285	4741
SOUND_MAX_LO	1288	4744
SOUND_MAX_HI	128B	4747
SOUND_MIN_LO	128E	4750
SOUND_MIN_HI	1291	4753

SOUND_DIRECTION	1294	4756
SOUND_STEP_LO	1297	4759
SOUND_STEP_HI	129A	4762
SOUND_FREQ_LO	129D	4765
SOUND_FREQ_HI	12A0	4768
TEMP_TIME_LO	12A3	4771
TEMP_TIME_HI	12A4	4772
TEMP_MAX_LO	12A5	4773
TEMP_MAX_HI	12A6	4774

TEMP_MIN_LO	12A7	4775
TEMP_MIN_HI	12A8	4776
TEMP_DIRECTION	12A9	4777
TEMP_STEP_LO	12AA	4778
TEMP_STEP_HI	12AB	4779

TEMP_FREQ_LO	12AC	4780

TEMP_FREQ_HI	12AD	4781
TEMP_PULSE_LO	12AE	4782
TEMP_PULSE_HI	12AF	4783
TEMP_WAVEFORM	12B0	4784
POT_TEMP_1	12B1	4785	Temporaries for 'POT' Function
POT_TEMP_2	12B2	4786
WINDOW_TEMP	12B3	4787
SAVRAM		12B7	4791	Used BY SPRDEF & SAVSPR
DEFMOD		12FA	4858	Used BY SPRDEF & SAVSPR
LINCNT		12FB	4859	Used BY SPRDEF & SAVSPR
SPRITE_NUMBER	12FC	4860	Used BY SPRDEF & SAVSPR
IRQ_WRAP_FLAG	12FD	4861	Used BY BASIC IRQ to BLOCK
				All BUT ONE IRQ CALL

		1300	4864	Application Program Area $1300-$1BFF

RAMBOT		1C00	7168	Start Of Basic Text $1C00-$EFFF
				(KERNAL sets MEMBOT here)

		1C00	7168	Video Matrix #2 (1KB of colors for
				Bitmap, if allocated) $1C00-$1FFF

		2000	8192	VIC BITMAP (8KB, if allocated)
				$2000-$3FFF


	BEGINNING OF ROM OVER RAM

		4000	16384	C128 BASIC LO ROM

				Start of BASIC Text if Bit Map
				is allocated (RAM) $4000-$EFFF

		8000	32768	C128 BASIC Hl ROM (or Function ROM) $8000-$BFFF



	BASIC JUMP TABLE


		BASIC ENTRY

JMP HARD_RESET	4000	16384	COLD ENTRY
JMP SOFT_RESET	4003	16387	WARM ENTRY
JMP BASIC_IRQ	4006	16390	IRQ ENTRY


		FORMAT CONVERSIONS

JMP AYINT	AF00	44800	Convert F.P. to Integer
JMP GIVAYF	AF03	44803	Convert Integer to F.P.

JMP FOUT	AF06	44806	Convert F.P. to ASCII String
JMP VAL_l	AF09	44809	Convert ASCII String to F.P.
JMP GETADR	AF0C	44812	Convert F.P. to an Address
JMP FLOATC	AF0F	44815	Convert Address to F.P.


		MATH FUNCTIONS

JMP FSUB	AF12	44818	MEM - FACC
JMP FSUBT	AF15	44821	ARG - FACC
JMP FADD	AF18	44824	MEM + FACC
JMP FADDT	AF1B	44827	ARG - FACC
JMP FMULT	AF1E	44830	MEM * FACC
JMP FMULTT	AF21	44833	ARG * FACC
JMP FDIV	AF24	44836	MEM / FACC
JMP FDIVT	AF27	44839	ARG / FACC
JMP LOG		AF2A	44842	Compute Natural LOG Of FACC
JMP INT		AF2D	44845	Perform BASIC INT On FACC
JMP SQR		AF30	44848	Compute Square Root OF FACC
JMP NEGOP	AF33	44851	Negate FACC
JMP FPWR	AF36	44854	Raise ARG to The Mem Power
JMP FPWRT	AF39	44857	Raise ARG to The FACC Power
JMP EXP		AF3C	44860	Compute EXP Of FACC

JMP COS		AF3F	44863	Compute COS Of FACC
JMP SIN		AF42	44866	Compute SIN Of FACC
JMP TAN		AF45	44869	Compute TAN Of FACC
JMP ATN		AF48	44872	Compute ATN Of FACC
JMP ROUND	AF4B	44875	Round FACC
JMP ABS		AF4E	44878	Absolute Value Of FACC
JMP SIGN	AF51	44881	Test Sign Of FACC
JMP FCOMP	AF54	44884	Compare FACC With Memory
JMP RND 0	AF57	44887	Generate Random F.P. Number


		MOVEMENT

JMP CONUPK	AF5A	44890	Move RAM MEM to ARG
JMP ROMUPK	AF5D	44893	Move ROM MEM to ARG
JMP MOVFRM	AF60	44896	Move RAM MEM to FACC
JMP MOVFM	AF63	44899	Move ROM MEM to FACC
JMP MOVMF	AF66	44902	Move FACC to MEM
JMP MOVFA	AF69	44905	Move ARG to FACC
JMP MOVAF	AF6C	44908	Move FACC to ARG


		OTHER BASIC ROUTINES

JMP OPTAB	AF6F	44911
JMP DRAWLN	AF72	44914


MEMORY
ADDRESS		HEXADECIMAL DECIMAL
LABEL		ADDRESS ADDRESS DESCRIPTION

		OTHER BASIC ROUTINES

JMP GPLOT	AF75	44917
JMP CIRSUB	AF78	44920
JMP RUN		AF7B	44923
JMP RUNC	AF7E	44926
JMP CLEAR	AF81	44929
JMP NEW		AF84	44932
JMP LNKPRG	AF87	44935
JMP CRUNCH	AF8A	44938

JMP FNDLIN	AF8D	44941
JMP NEWSTT	AF90	44944
JMP EVAL	AF93	44947
JMP FRMEVL	AF96	44950
JMP RUN_A_PROGRAM
		AF99	44953

JMP SETEXC	AF9C	44956
JMP LINGET	AF9F	44959
JMP GARBA2	AFA2	44962
JMP EXECUTE_A_LINE
		AFA5	44965


		MONITOR ENTRY

JMP CALL	B000	45056	MONITOR Call Entry

JMP BREAK	B003	45059	MONITOR Break Entry
JMP MONCMD	B006	45062	MONITOR Command Parser Entry
		C000	49152	KERNAL (or Function) ROM $C000-$FFFF


		EDITOR JUMP TABLE

JMP CINT	C000	491S2	Initialize Editor & Screen
JMP DISPLY	C003	49155	Display Charac in .A, Color

JMP LP2		C006	49158	Get Key From IRQ Buffer

JMP LOOP5	C009		Into A

JMP PRINT	C00C	49164	Print Character In .A
JMP SCRORG	C00F	49167	Get # of Scrn Rows, Cols Into X & Y

JMP SCNKEY	C012	49170	Scan Keyboard Subroutine
JMP REPEAT	C015	49173	Handle Repeat Key & Store Decoded Key
JMP PLOT	C018	49176	Read Or Set CRSR Position In X, Y
JMP CURSOR	C01B	49179	Move 8563 Cursor Subroutine
JMP ESCAPE	C01E	49182	Execute ESC Function using chr in .A
JMP KEYSET	C021	49185	Redefine A Programmable Func'n Key
JMP IRQ		C024	49188	IRQ Entry
JMP INIT80	C027	49191	Initialize 80-Column Character Set
JMP SWAPPER	C02A	49194	Swap Editor Locals (in 40/80 change)
JMP WINDOW	C02D	49197	Set Top-Left or Bot-Right of Window
		D000	53248	VIC Character ROM ($D000-$DFFF)


		VIC CHIP REGISTERS

VICREG0		D000	53248	Sprite 0, X-Location
VICREG1		D001	53249	Sprite 0, Y-Location
VICREG2		D002	53250	Sprite 1, X-Location
VICREG3		D003	53251	Sprite 1, Y-Location
VICREG4		D004	53252	Sprite 2, X-Location
VICREG5		D005	53253	Sprite 2, Y-Location
VICREG6		D006	53254	Sprite 3, X-Location
VICREG7		D007	53255	Sprite 3, Y-Location
VICREG8		D008	53256	Sprite 4, X-Location
VICREG9		D009	53257	Sprite 4, Y-Location
VICREG10	D00A	53258	Sprite 5, X-Location
VICREG11	D00B	53259	Sprite 5, Y-Location
VICREG12	D00C	53260	Sprite 6, X-Location
VICREG13	D00D	53261	Sprite 6, Y-Location
VICREG14	D00E	53262	Sprite 7, X-Location
VICREG15	D00F	53263	Sprite 7, Y-Location
VICREG16	D010	53264	M.S. Bit of X-Location for Sprites 0 - 7



	THE COMMODORE 128 AND COMMODORE 64 MEMORY MAPS


		KERNAL JUMP TABLE
		New Entries For C128

JMP SPIN SPOUT	FF47		65351	Set up Fast Serial Port for I/O
JMP CLOSE ALL	FF4A		65354	Close All Logical Files for a device
JMP C64MODE	FF4D		65357	Reconfigure System as a C64 (no return)
JMP DMA CALL	FF50		65360	Initiate DMA Request to External RAM
					Expansion, Send command to DMA Device

JMP BOOT CALL	FF53		65363	Boot Load Program From Disk
JMP PHOENIX	FF56		65366	Call All Function Cards' Cold Start
					Routines, Initialize

JMP LKUPLA	FF59		65369	Search Tables For Given LA
JMP LKUPSA	FF5C		65372	Search Tables For Given SA
JMP SWAPPER	FF5F		65375	Switch Between 40 and 80 Columns (Editor)
JMP DLCHR	FF62		65378	Init 80-Col Character RAM (Editor)
JMP PFKEY	FF65		65381	Program Function Key (Editor)
JMP SETBNK	FF68		65384	SET Bank For I/O Operations
JMP GETCFG	FF6B		65387	Lookup MMU Data For Given Bank
JMP JSRFAR	FF6E		65390	JSR to Any Bank, RTS to Calling Bank
JMP JMPFAR	FF71		65393	JMP to Any Bank
JMP INDFET	FF74		65396	LDA (FETVEC),Y FROM Any Bank
JMP INDSTA	FF77		65499	STA (STAVEC),Y to Any Bank
JMP INDCMP	FF7A		65402	CMP (CMPVEC),Y to Any Bank
JMP PRIMM	FF7D		65405	Print Immediate Utility
					(Always JSR to this routine)


		STANDARD KERNAL JUMP TABLE

		FF80		65408	Release Number Of KERNAL
JMP CINT	FF81		65409	Init Editor & Display
JMP IOINIT	FF84		65412	Init I/O Devices (ports, timers, etc.)
JMP RAMTAS	FF87		6S415	Initialize RAM And Buffers For System
JMP RESTOR	FF8A		65418	Restore Vectors to Initial System
JMP VECTOR	FF8D		65421	Change Vectors For USER
JMP SETMSG	FF90		65424	Control O.S. Message
JMP SECND	FF93		65427	Send SA After LISTEN
JMP TKSA	FF96		65430	Send SA After TALK
JMP MEMTOP	FF99		65433	Set/Read Top Of System RAM
JMP MEMBOT	FF9C		65436	Set/Read Bottom Of System RAM
JMP KEY		FF9F		65439	Scan Keyboard (Editor)
JMP SETTMO	FFA2		65442	Set Timeout In IEEE (reserved)
JMP ACPTR	FFA5		65445	Handshake Serial Byte In
JMP CIOUT	FFA8		65448	Handshake Serial Byte Out
JMP UNTLK	FFAB		65451	Send UNTALK Out Serial
JMP UNLSN	FFAE		65454	Send UNLISTEN Out Serial
JMP LISTN	FFB1		65457	Send LISTEN Out Serial
JMP TALK	FFB4		65460	Send TALK Out Serial
JMP READSS	FFB7		65463	Return I/O Status Byte
JMP SETLFS	FFBA		65460	Set LA, FA, SA
JMP SETNAM	FFBD		65469	Set Length And File Name Address
JMP (IOPEN)	FFC0	OPEN	65472	OPEN Logical File
JMP (ICLOSE)	FFC3	CLOSE	65475	CLOSE Logical File
JMP (ICHKIN)	FFC6	CHKIN	65478	Set Channel In
JMP (ICKOUT)	FFC9	CKOUT	65481	Set Channel Out
JMP (ICLRCH)	FFCC	CLRCH	65484	Restore Default I/O Channel
JMP (IBASIN)	FFCF	BASIN	65487	INPUT From Channel
JMP (IBSOUT)	FFD2	BSOUT	65490	OUTPUT To Channel
JMP LOADSP	FFD5		65493	LOAD From File
JMP SAVESP	FFD8		65496	SAVE to File
JMP SETTIM	FFDB		65599	Set Internal Clock
JMP RDTIM	FFDE		65502	Read Internal Clock
JMP (ISTOP)	FFE1	STOP	65505	Scan STOP Key
JMP (IGETIN)	FFE4	GETIN	65508	Read Buffered Data
JMP (ICLALL)	FFE7	CLALL	65511	Close All Files And Channels
JMP UDTIM	FFEA	CLOCK	65514	Increment Internal Clock
JMP SCRORG	FFED		65517	Return Screen Window Size (Editor)
JMP PLOT	FFF0		65520	Read/Set X,Y Cursor Coord (Editor)
JMP IOBASE	FFF3		65523	Return I/O Base
SYSTEM		FFF8		65528	Operating System Vector (RAM1)
NMI		FFFA		65530	Processor NMI Vector
RESET		FFFC		65532	Processor RESET Vector
IRQ		FFFE		65534	Processor IRQ/BRK Vector



		KERNAL/EDITOR FLAGS AND SHADOW REGISTERS

The following symbols are used by the C128 Editor. Note that the Editor IRQ
VIC screen handler depends upon them. In most cases the contents of these
locations will be placed directly into the appropriate register and should be
used instead of the actual register. For example, to change the location of the
character set used by VIC, use VM1 ($0A2C) instead of VIC register 24 ($D018).
VM1 will be used by the editor to update VIC register 24.


ADDRESS NAME	EXPLANATION

$00D8/GRAPHM	See below. IF = $FF THEN EDITOR LEAVES VIC ALONE.
$00D9/CHAREN	MASK For 8502 /CHAREN BIT.
$0A2C/VM1	VIC Text Mode Video Matrix & Character Base Pointer.
$0A2D/VM2	VIC Graphic Mode Video Matrix & Bit Map Pointer.
$0A2E/VM3	8563 TEXT DISPLAY BASE Address.
$0A2F/VM4	8S63 ATTRIBUTE BASE Address.
$0A34/SPLIT	IN SPLIT SCREEN MODE, CONTAINS VALUE For MIDDLE RASTER IRQ.
$0A2B/CURMOD	8563 CURSQR Mode.
$0A21/PAUSE	CONTROL S Flag (In effect = $13)



540 COMMODORE 128


	EXPLANATION OF VARIOUS KERNAL/EDITOR FLAG BYTES, ETC.

ADDRESS SYMBOL			DESCRIPTION

		7	6	5	4	3	2	1	0


0000	D6510	-	(IN)	(OUT)	(IN)	(OUT)	(OUT)	(OUT)	(OUT)
0001	R6510	-	CAPKEY	CASMTR	CASSEN	CASWRT	CHAREN	HIRAM	LORAM

00F7	LOCKS	CASE	CTL S	-	-	-	-	-	-

00F8	SCROLL	OFF	LINKER

00D3	SHFLAG	-	-	-	ALT	ALPHA	CTRL		SHIFT

OA22	RPTFLG	ALL	NONE	-	-	-	-	-	-

OA26	BLNON	ON	BLNK	-	-	-	-	-	-

00F9	BEEPER	ON	-	-	-	-	-	-	-

00D8	GRAPHM	MCM	SPLIT	BMM	-	-	-	-	-

00D7	MODE	40/80	-	-	-	-	-	-	-

OA04	INIT_	CHRSET	CINT	-	-	-	-	-	BASIC
	STATUS



Notes on Kernal Symbols:

Init_Status. See also above. Lets system know what has been initialized and
what hasn't. Set to $00 by a reset but untouched by NMI.

System_Vector. Where the Kernal goes when it has to go somewhere. It's set
to BASIC cold at reset. BASIC itself sets it to BASIC warm after it has
initialized. The monitor respects it too.

System. Vector in RAM1 at $FFF8. Set at power-up to C128MODE, user may redirect
it to his code. Taken at reset always providing user with control (protection)
from reset.


<end>